## Slide 1: Passively Powered pH Sensor for Gastric Disorder Analysis
Nicholas Piaquadio
Project Team Members:
Tucker Lundgren
Kevin Hart
Sean Hart
Advisor: Dr. Reena Dahle

## Slide 2: Motivation
74 percent of Americans report Gastro-Intestinal discomfort [1]
Many diseases are related to stomach pH:
Gastroesophageal reflux disease (GERD)
Stomach Ulcers/ Gastritis
Stomach Cancer

## Slide 3: Solution
Implantable Tag
  No Battery
  Wireless Operation
Wearable Reader
  Chic Fanny Pack

## Slide 4: Delivered Design
Modeled Stomach
Regular pH Sensor
Applications
Animal Testing Alternative
Non-invasive in vivo testing
Real digestive motion for antacid testing

## Slide 5: Overview

## Slide 6: Design Constraints
IEEE-C95.1-2005 (Regulation on Human Exposure to RF EM Fields)
Small Transponder Size
Accurate pH Readings
Maximized Read Range
Budget - $600

## Slide 7: Theory: Inductive Coupling and Energy Harvesting
A changing magnetic field inside a coil induces a voltage by Faraday’s Law:
Neumann’s Formula Gives the mutual inductance:

## Slide 8: Theory: FSK Modulation
Frequency- Shift Keying
Power is in a high frequency carrier
Signal is a low frequency amplitude change

## Slide 9: Electronics Design- Simulation
ADS Schematic: Each block is a functional circuit

## Slide 10: Electronics Design- Breadboarding
Reader V2
Reader V1
Implant V1

## Slide 11: PCB Layouts - EAGLE
-Computer Aided Design: lay out circuit board
Copper Traces in blue + red
Vias in green
Double- Sided

## Slide 12: Reader Layout – Single Sided

## Slide 13: Finished Electronics - Implant
Bulky pH Probe
Waterproof Coating
Coil Wrapped Around Board
Pins Simulate Microneedles

## Slide 14: Finished Reader

## Slide 15: Injection Molding
3D Printed Core
Mold for Wax Core
Injection
Stomach

## Slide 16: Chemical Test Results
Solution | A.D.A. pH [3] | System pH | % Error
pH 4 Buffer | 4.00 | 4.00 | 0.12
Pepsi Original | 2.40 | 2.46 | 2.57
Vitamin Water | 3.05 | 2.88 | -5.75
Grape Juice | 3.30 | 3.22 | -2.58
Grapefruit Juice | 3.22 | 3.30 | 2.42
Lemon Juice* | 2.25 | 2.46 | 8.69
* Not Standard Brand |  |  | 
pH Measurements of Beverages:
Antacid Testing:

## Slide 17: Read Range
Took Readings on XY table
Max distance of 3.5’’

## Slide 18: Conclusion
Battery-less Implant + Test Setup
Iterative Design Process
System returns accurate pH out to 3.5’’
Future improvement calls for micromachining

## Slide 19: References
[1]“Survey shows 74 percent of Americans living with GI discomfort,” Fox News, 24-Nov-2013. [Online]. Available: http://www.foxnews.com/health/2013/11/22/survey-shows-74-percent-americans-experience-gi-discomfort.html. [Accessed: 18-Sep-2018].
[2] “Esophageal pH monitoring,” Medigus, 2005. [Image] [Online] Available: http://www.medigus.com/healthcare-professional/clinical-presentations/119-recent-advances-in-diagnostic-testing-for-gastroesophageal-reflux-disease [Accessed:17-Sep-2018]
[3] American Dental Association . The pH of beverages in the United States. [online] Ada.org. [Accessed 16 Apr. 2019].